## Slide 1: Deep Neural Network based Stable Digital Predistortion using ELU Activation for Switchless Class-G Power Amplifier
Presenter：Xiaoqi Yu
（Date）18/05/2024

## Slide 2: Contents
1、Background & Introduction
2、The proposed Digital Predistortion Algorithm
3、Experimental validation & Discussion
4、Conclusion

## Slide 3: 1. Background & Introduction
Digital Predistortion(DPD) is a crucial linearization techni-que for Power Amplifier (PA). Fig. 1 and Fig. 2 show the fundamental principle and indirect structure of DPD algorithm in the paper. It is the most vital to model the PA precisely.
Fig. 1. Fundamental principle (left) and block diagram of DPD system with indirect learning architecture (right).
Back propagation (BP) neural network and its variations have attracted extensive research interest in modeling, especially real-valued focused time-delay neural network (RVFTDNN)[1][2].
Fig. 2. BP neural network (left) and RVFTDNN [1][2].
[1] M. Rawat, K. Rawat, and F. M. Ghannouchi, “Adaptive digital predistortion of wireless power amplifiers/transmitters using dynamic real-valued focused time-delay line neural networks,” IEEE Trans. Microw. Theory Techn., vol. 58, no. 1, pp. 95–104, Jan. 2010.
[2] Taijun Liu, S. Boumaiza and F. M. Ghannouchi, "Dynamic behavioral modeling of 3G power amplifiers using real-valued time-delay neural networks," in IEEE Transactions on Microwave Theory and Techniques, vol. 52, no. 3, pp. 1025-1033, March 2004, doi: 10.1109/TMTT.2004.823583.

## Slide 4: 1. Background & Introduction
In 2019, augmented real-valued time-delay neural network (ARVTDNN) based DPD was proposed which toke into account the envelope-dependent terms [3]. It is proved that solve the dc offset, I/Q imbalance, and nonlinear PA distortions of a transmitter system by one-step (Fig. 4).
Fig. 3. Block diagram of ARVTDNN[3].
The adding envelope-dependent terms make the proposed model generate richer basis function set, which further improve the modeling accuracy.
Fig. 4. Characteristics of the transmitter system. (Left) Gain characteristics.
(Right) Phase characteristics.[3].
[3] D. Wang, M. Aziz, M. Helaoui and F. M. Ghannouchi, "Augmented Real-Valued Time-Delay Neural Network for Compensation of Distortions and Impairments in Wireless Transmitters," in IEEE Transactions on Neural Networks and Learning Systems, vol. 30, no. 1, pp. 242-254, Jan. 2019.
Fig. 5. Sigmoid activation of common BP NN.

## Slide 5: 2. The proposed DPD
Fig. 6. The proposed Deep neural network (DNN) model.
Fig. 7. The activations of neural networks (left) and the expression of ELU in the paper (right).
Fig. 6 indicates the structure of the proposed deep neural network of DPD, which is based on the ARVTDNN structure. The proposed DNN adopts 9 hidden layers where each contains 10 neurons and delay tap (m) and nonlinear order (k) are set to 2 and 4, respectively.
To speed up the convergence of DNN and enhance the modeling accuracy, we utilize exponential linear unit (ELU) instead of Sigmoid/ReLU in this paper, which can avoid the gradient vanishing problem and ReLU inactive problem. [4][5]
[4] R. Hongyo, Y. Egashira and K. Yamaguchi, "Deep Neural Network Based Predistorter with ReLU Activation for Doherty Power Amplifiers," 2018 Asia-Pacific Microwave Conference (APMC), Kyoto, Japan, 2018, pp. 959-961.
[5] Lu, Lu, et al. "Dying relu and initialization: Theory and numerical examples." arXiv preprint arXiv:1903.06733 (2019).

## Slide 6: 2. The proposed DPD
Fig. 8. The activation of neural network. Sigmoid (Left), ReLU (Middle) and ELU (Right).
The derivative of activation is important for the convergence speed and accuracy of backpropagation (BP) algorithm.
Some problems can be avoided by using ELU in deep neural network back-propagation process.[4][5]
Fig. 9. Simple representation of gradient descent algorithm in backpropagation process.
[4] R. Hongyo, Y. Egashira and K. Yamaguchi, "Deep Neural Network Based Predistorter with ReLU Activation for Doherty Power Amplifiers," 2018 Asia-Pacific Microwave Conference (APMC), Kyoto, Japan, 2018, pp. 959-961.
[5] Lu, Lu, et al. "Dying relu and initialization: Theory and numerical examples." arXiv preprint arXiv:1903.06733 (2019).
Fig. 10. Negative-valued I/Q samples cause parts of neuron inactive in backpropagation process .
BP process
Small gradient
Zero gradient
Speed up the gradient descent algorithm.

## Slide 7: 3. Experimental validation
Fig. 11. The SLCG PA used in the experiment.
Fig. 12. The modulated signal measurement results of the SLCG PA under 10MHz 64QAM signals.[6]
SLCG PA is a recently developed back-off efficiency enhancement (BEE) technique that adopts two-quadrant modulation (TQM). The BEE technique brings new challenges for PA linearization.
SLCG PA shows poor linearity and linearizability under wideband modulated signal excitations.
[6] X. Fang, R. Chen and J. Shi, "Switchless Class-G Power Amplifiers: Generic Theory and Design Methodology Using Packaged Transistors," in IEEE Transactions on Microwave Theory and Techniques, doi: 10.1109/TMTT.2024.3351852.

## Slide 8: 3. Experimental validation
Fig. 13. Diagram of the proposed DPD measurement testbench.
In this measurement, the above SLCG PA was excited with 256QAM signals at the center frequency of 2.4GHz with various modulation bandwidths varying from 20MHz to 200MHz, and further linearized using various DPD methods at a of 30dBm with a of 38%.
The proposed DPD algorithm is implemented in MATLAB to process the RF signal received by the spectrum analyzer (Rohde & Schwarz FSW48).
Fig. 14. Indirect learning (IL) structure of the proposed DPD.
[6] X. Fang, R. Chen and J. Shi, "Switchless Class-G Power Amplifiers: Generic Theory and Design Methodology Using Packaged Transistors," in IEEE Transactions on Microwave Theory and Techniques, doi: 10.1109/TMTT.2024.3351852.

## Slide 9: 3. Experimental validation
Fig. 15. Normalized Gain distortion with and w/o the proposed DPD.
The SLCG PA shows intense nonlinearity and memory effect under the wideband signal excitations (200MHz 256QAM modulated signals) .
When apply the proposed DPD technique, the intense distortion of normalized gain and phase has been mitigated substantially (Fig. 15 and Fig. 16).
Fig. 16. Phase distortion with and w/o the proposed DPD.
With DPD
Without DPD
With DPD
Without DPD

## Slide 10: 3. Experimental validation
Fig. 17. The PA output power spectral density with and without DPD.
Comparing existing DPD methods, the proposed one offers a 4-8.4dB improvement in ACPR as well as about 1.3-4.3dB improvement in NMSE. Also, by applying ELU function in deep neural network, the training process can be accelerated about 3-4 times compared with Sigmoid (Fig. 17 and Table. 1) .
Fig. 18 illustrates the DPD results for the signal modulation bandwidth swept from 20MHz to 200MHz. The proposed DPD method can realize effective linearization for the nonlinear PA excited with wideband modulated signals.
Table. 1. Performance of DPDs applied to SLCG PA under 200MHz 256QAM signals.
Fig. 18. The DPD measurement results under various modulation bandwidths.

## Slide 11: 4、Conclusion
Efficient: This paper proposes a deep ARVTDNN DPD technique, which employs ARVTD-based input vector and adopts ELU function to replace the sigmoid one in the neuron activation, and consequently avoids the gradient vanishing problem and accelerates the DNN training.
Stable: Experimental verification conducted on an SLCG PA demonstrates that the proposed DPD maintains excellent linearization performance and enhanced stability in the case of large signal modulation bandwidth.

## Slide 12: Reference
[1] M. Rawat, K. Rawat, and F. M. Ghannouchi, “Adaptive digital predistortion of wireless power amplifiers/transmitters using dynamic real-valued focused time-delay line neural networks,” IEEE Trans. Microw. Theory Techn., vol. 58, no. 1, pp. 95–104, Jan. 2010.
[2] Taijun Liu, S. Boumaiza and F. M. Ghannouchi, "Dynamic behavioral modeling of 3G power amplifiers using real-valued time-delay neural networks," in IEEE Transactions on Microwave Theory and Techniques, vol. 52, no. 3, pp. 1025-1033, March 2004, doi: 10.1109/TMTT.2004.823583.
[3] D. Wang, M. Aziz, M. Helaoui and F. M. Ghannouchi, "Augmented Real-Valued Time-Delay Neural Network for Compensation of Distortions and Impairments in Wireless Transmitters," in IEEE Transactions on Neural Networks and Learning Systems, vol. 30, no. 1, pp. 242-254, Jan. 2019.
[4] R. Hongyo, Y. Egashira and K. Yamaguchi, "Deep Neural Network Based Predistorter with ReLU Activation for Doherty Power Amplifiers," 2018 Asia-Pacific Microwave Conference (APMC), Kyoto, Japan, 2018, pp. 959-961.
[5] Lu, Lu, et al. "Dying relu and initialization: Theory and numerical examples." arXiv preprint arXiv:1903.06733 (2019).
[6] X. Fang, R. Chen and J. Shi, "Switchless Class-G Power Amplifiers: Generic Theory and Design Methodology Using Packaged Transistors," in IEEE Transactions on Microwave Theory and Techniques, doi: 10.1109/TMTT.2024.3351852.
[7] M. T. Hagan and M. B. Menhaj, "Training feedforward networks with the Marquardt algorithm," in IEEE Transactions on Neural Networks, vol. 5, no. 6, pp. 989-993, Nov. 1994.
[8] Haykin, Simon, and N. Network. "A comprehensive foundation." Neural networks 2.2004 (2004): 41.
[9] F. M. Ghannouchi and O. Hammi, "Behavioral modeling and predistortion," in IEEE Microwave Magazine, vol. 10, no. 7, pp. 52-64, Dec. 2009.

## Slide 13: Thank you! Q&A